## Slide 1: Flow-Through Uroflow Device
Group 32
Akhil Sundar (presenter),
Jodi Small, Jordan Nick

## Slide 2: Need
Diagnose urinary system issues
  50% of men over 40
Diseases
  Bladder outlet obstruction
  Low bladder pressure
  Enlarged prostate

## Slide 3: Current Technology
Expensive
Excessive clean up
Frequent maintenance
Miscalculation
  Low flow data

## Slide 4: Scope
Create a flow-through uroflow system that measures either volume or flow rate and calculates the other in real-time.
Notes: Flow –through means we want the urine to flow into a toilet, and not have to be transferred from a beaker to a toilet

## Slide 5: Design Specifications

## Slide 6: Alternatives: Funnel
Disposable funnel
  Proper material
Reusable funnel
  Requires cleaning
  Releasable bottom
No funnel
Notes: Flow –through means we want the urine to flow into a toilet, and not have to be transferred from a beaker to a toilet

## Slide 7: Alternatives: RGB Camera
Separate urine from background
With funnel
  Translucent funnel
  Measure urine levels
Without funnel
  2 cameras
  Cross-sectional area and height
Issues: comfort and accuracy
Notes: Measure urine levels from height and cross sectional area, differentiate to find flow rate.
w/o funnel, calculate volume in discrete periods of time,

## Slide 8: Alternatives: Thermal Imaging
Easy to visualize urine
With funnel
  Conduct heat
Without funnel
  Similar to RGB
Issues: accuracy and cost

## Slide 9: Alternatives: Optical Sensors
Measures flow rate
Uses refractive indexes
Accurate
Requires funnel
Issues
  Unsanitary
  Space
Figure 1: (a) air disperses light. (b) liquid focuses light
Notes: Sensors have to be right up against funnel, so disposable is no option. Sensors have to be removed during any cleaning, which is complicated and unsanitary. The column being measured has to be very thin, and creating space is an issue

## Slide 10: Alternatives: Ultrasound Imaging
Requires a funnel
Image fluid in funnel
Issues
  Air barrier
  Unsanitary maintenance

## Slide 11: Alternatives: Transmitting Bob
Floating sensor using radar
Can do with or without funnel
Measures volume
  Detects urine level
  Known funnel/toilet geometry
Issues: cleaning and accuracy
Notes: Accuracy issues are due to low flow

## Slide 12: Alternatives: Force Transducer
Force plate inside toilet
Used in some current devices
  Not flow through
High refresh rate
Measure volume
Issues
  Splashing if no funnel

## Slide 15: Final Options
Disposable funnel with bob
Reusable funnel with bob
No funnel with bob
Force plate with funnel/basin
Notes: Decided not to go with bob technology because of cleaning issues, and our client Laborie already has the force plate technology but it is used in a non-flow through environment

## Slide 16: Chosen Design
Reusable basin
Cup with force plate
Releasable bottom
Measures volume
Figure 2: Initial sketches

## Slide 17: Chosen Design

## Slide 18: Chosen Design
Uses current technology
Minimizes splashing
Easy to clean
Can adapt Bluetooth

## Slide 19: Design Schedule

## Slide 20: Team Responsibilities

## Slide 21: Thank You
Questions?

## Slide 22: Figures
1. Nguyen, Nam-Trung, and Thai-Quang Troung. “Flow rate measurement in microfluidics using optical sensors.” 1st international conference on sensing technology, Palmerston North. 2005.